2.
A.
a. 46281
b. 53
c. 40
d. 32 - 8 = 24 bytes
e. Client to Server
f. UDP
g. Yes it is calculated.

B.
For DNS query message:
Source IP: 172.16.59.61
Destination IP: 172.16.19.202

For Response message:
Source IP: 172.16.19.202
Destination IP: 172.16.59.61

They are the addresses between which communication is happening.

C.
For DNS query message:
Source Port: 46281
Destination Port: 53

For Response message:
Source Port: 53
Destination Port: 46281

53 is a well-known port number.

D. Length of the first packet is 40, it carries 32 bytes of payload.

2b.
Part 1:

1. 172.16.59.82:7680
2. Only the Don’t fragment bit is set
3. Sequence Number is 0
Acknowledgement Number is 1
4. Window size: 65535

Part 2:

1. Acknowledge and Push bit is set
2. 153 – 32 = 121
3. 0.00026 seconds
4. 87 – 32 = 55 bytes per packet. The sequence number increases by the number of bytes transmitted, and the acknowledgement number increases by the number of bytes recieved.
5. While sending the GET request, window size was 64256, and while recieving the OK request, window size was 65024, with the initial window sizes 502 and 508 and both having the same scaling factor – 128. Window sizes will change to avoid congestion.

6. By reducing or increasing window size, the server and client each ensure that the other device sends data just as fast as the recipient can deal with it.

7. That code represents a successful retrieval of the document ("OK").
If the server failed to retrieve the document, the status codes provide more information, like if the failure was due to user error or server error.

Part 3:

1. 4 segments are exchanged – FIN, ACK, FIN, ACK
2. Client initiated the connection termination phase
3. FIN and ACK flags are set.